## Slide 1: Relational STE and Theorem Proving for Formal Verification of Industrial Circuit Designs
John O’Leary and Roope Kaivola, Intel
Tom Melham, Oxford

## Slide 2: CPU datapath verification at Intel
Thousands of operations
  Integer, FP, SSE, AVX, …
  “Miscellaneous”
  Various operating modes, flags, faults
Live RTL, changing frequently until a few weeks before tapeout

## Slide 3: Scaling up
Tens of designs
Different optimization points
Different teams
Different countries
Not only CPUs
Not all have FV experts on staff

## Slide 4: Integer multiplier
S1 =  BEi * 2ki
PPi = S2 * BEi
P =  PPi * 2ki
Partial Products Generation
Booth
Encoder
Wallace Tree Adder Network
S1
S2
PROD
BEi
PPi

## Slide 5: The multiplier zoo
10-20 multipliers
Hand designed
Hand optimized
All different
Partial Products Generation
Booth
Encoder
Wallace Tree Adder Network
S1
S2
PROD
BEi
PPi

## Slide 6: FV challenges
Varying specs and verification strategies
  Implementation changes from design to design
  Multiplier always requires decomposition
Ten designers but not ten multiplier FV experts
Same story for integer, MMX, FP, SSE, GPU flavors of multiplication, addition, division, …
  Some operations require even more intricate decomposition

## Slide 7: The solution
Parameters
CVE
Per-design specs
Verification runs
Deduction
Development
Regression

## Slide 8: The solution done right
An executable logic for writing the specs and verification scripts: reFLect
A symbolic simulator that admits relational specifications written in logic: rSTE
A tightly integrated theorem prover for executing the deductive proofs: Goaled

## Slide 9: The solution done right
An executable logic for writing the specs and verification scripts: applicative common lisp
A symbolic simulator that admits relational specifications written in logic: ESIM+GL
A tightly integrated theorem prover for executing the deductive proofs: ACL2
[Slobodová et al, MEMOCODE’11]

## Slide 10: The reFLect Language
Core syntax:
  n,o,p ::= k | v | n o | p. n  o |  n  | ^n:s
… plus extensions driven by necessity
  BDDs built in as a primitive type
  Quotient types
  Overloading
  Named function parameters
  Records
  Possibly unsafe features: references, I/O, recursion
pattern matching
reflection

## Slide 11: Higher Order Logic of reFLect
HOL, following Church:
  Logic =
The reFLect logic:
  Logic =
-calculus
+
logical constants
+
rules
Basic idea in both systems:
  n  p means ├ n = p
  Define , , etc by axioms
  Add rules for function equality
  Proof by evaluation
reFLect
+
logical constants
+
rules

## Slide 12: Goaled Theorem Prover
LCF-style implementation, following in the footsteps of HOL and HOL Light
  Thm is a protected data type, constructible only through a small set of trusted function calls (a.k.a. inference rules)
Features driven by necessity
  Theories: of reFLect data types, natural numbers, integers, rationals, lists, pairs, reFLect ADTs
  Proof automation: rewriting, first order solving, linear arithmetic
  Bitstring arithmetic
  Support for the reflect language extensions

## Slide 13: The last bit
An executable logic for writing the specs and verification scripts: reFLect
A symbolic simulator that admits relational specifications written in logic: rSTE
A tightly integrated theorem prover for executing the deductive proofs: Goaled

## Slide 14: Limitations of STE
Trajectory assertion:
  ckt |= [[ S is v ==>> (BEi is fi(v)) ]]
But,
  You need a special purpose reasoning system for this special purpose logic
  Relational specifications cannot be expressed directly
Booth
Encoder
S
BEi

## Slide 15: Relational STE
STE’s antecedent and consequent are replaced with lists of constraints
  A constraint is a relationship between a finite set of circuit nodes at specified points in time
Idea:
  rSTE ckt cin cout means “In any behavior of ckt in which all of the constraints cin hold, all of the constraints cout hold”

## Slide 16: Relational STE Intuition
rSTE ckt
[] []
Full Add
ci
a
b
s
c

## Slide 17: Constraints
A constraint c has three components:
  name(c) : string
  sig(c) :
  pred(c) :
The behavior of the circuit is also formulated as a constraint:

## Slide 18: From Relational STE to Logic
Theorem:
For lists of constraints,

## Slide 19: Relational STE in Action
Define boothc such that
  )
Then, rSTE ckt [] [boothc] → T implies
Booth
Encoder
S1
BEi

## Slide 20: Relational STE in Action
s2i e s1)
Booth
Encoder
S1
BEi

## Slide 21: Completing a Multiplier proof
Partial Products Generation
Booth
Encoder
Wallace Tree Adder Network
S1
S2
PROD
BEi(S1)
PPi

## Slide 22: Proof engineering
Additional arguments to rSTE
  Constant antecedent: clock, reset
  rSTE options: bdd variable ordering, param, …
  Not shown here, but see paper
Analysis of CVE verification scripts
  N layers of function calls between input parameters and generation of specs
  Much deductive effort toward exposing the specs
  Routine rewriting, also not shown here

## Slide 23: Status and prospects
reFLect and rSTE are the main workhorses of datapath verification across Intel
Frameworks for integer and FP multipliers, FMAs, adders, divide/sqrt are widely deployed
Goaled checking of integer multipliers is used on a mainline design project and being pushed to others
We plan to integrate Goaled checking with our other frameworks